## Slide 1
ANIMATED IDLE SCREEN
RASPBERRY PI 5 · ON-DEVICE · OFFLINE
Face-Recognition
Attendance Kiosk
An offline check-in station that recognizes faces, greets each person by name, and logs attendance to a daily sheet — running entirely on a Raspberry Pi.
python · mediapipe · dlib · pygame · opencv

## Slide 2
OVERVIEW
What it does
The kiosk turns a Pi, a camera and a screen into a self-serve attendance station.
When someone steps up, its animated eyes lock on, it recognizes them from a photo database, shows a personalized greeting, and records the check-in.
No cards. No app. No internet.
100%
On-device & offline
30
FPS fluid animated UI
4×/s
Recognition checks
1/day
Logged per person
FACE ATTENDANCE KIOSK
02 / 14

## Slide 3
CONTEXT
Why face recognition?
Manual register
pen & paper
Roll call eats lesson time, any friend can answer for an absentee, and sheets must be re-typed later.
× slow · proxy-friendly
RFID / ID card
tap a token
Authenticates the card, not the person — cards get borrowed, shared and lost.
× verifies the token
Fingerprint
contact biometric
Verifies the person, but everyone touches one shared sensor and queues build at the door.
× contact · slow queues
Face recognition
this project
Nothing to carry or remember, hard to fake casually — a glance at the camera marks you present.
✓ contactless · on-device
The face is the one credential that can’t be forgotten, shared or lost — and it needs no contact at all.
FACE ATTENDANCE KIOSK
03 / 14

## Slide 4
EXPERIENCE
Designed to feel alive
Eyes that follow you
MediaPipe tracks your face; the pupils and eyelids react in real time.
Instant, personal greeting
“Good Morning, <name>” with your photo and role the moment you're recognized.
Live at a glance
Today's headcount and the last few arrivals sit on the idle screen.
ATTENDANCE
09:41 AM
Good Morning,
Anil Kumar
Student · Signass
✓ ATTENDANCE MARKED · 09:41 AM
recent 09:38 Anirban · 09:31 Abhinav
FACE ATTENDANCE KIOSK
04 / 14

## Slide 5
HOW IT WORKS
The check-in loop
IDLE
eyes idle, waiting for a face
VERIFY
recognizing — up to 5 s
GREET
known: photo, name, mark
COOLDOWN
brief pause → back to idle
UNKNOWN
no match → “not recognized”
The kiosk waits, verifies, then greets and logs the visitor — or shows not recognized after five seconds. A short cooldown stops the same person being logged twice.
FACE ATTENDANCE KIOSK
05 / 14

## Slide 6
ARCHITECTURE
How the data flows
Camera
live feed
cv2 grabber thread
Face Detection
MediaPipe mesh
bot_vision.py
Face Recognition
dlib · 128-D vector
face_recognition
Attendance Check
once per day
bot_attendance.py
Greet & Log
known person
Not Recognized
no match within 0.42
Every stage runs on the Raspberry Pi itself — no network, no cloud. Recognition happens on a background thread, and both outcomes are drawn to the fullscreen pygame display by the UI loop.
FACE ATTENDANCE KIOSK
06 / 14

## Slide 7
RECOGNITION
From face to record, in four steps
01
DETECT
MediaPipe FaceMesh
468-point mesh finds and frames the face on a 320×240 preview.
›
02
ENCODE
dlib ResNet
The face crop becomes a 128-number vector — its numeric fingerprint.
›
03
MATCH
Nearest neighbour
Compared to every known vector; a distance under 0.42 is a match.
›
04
LOG
Daily CSV
Matched name is written once per person to today's attendance sheet.
FACE ATTENDANCE KIOSK
07 / 14

## Slide 8
STACK
Built from open-source parts
Python 3.11
Core runtime & glue
Raspberry Pi 5
Edge hardware — camera + touchscreen
MediaPipe
Face detection & mesh tracking
face_recognition
dlib 128-D face matching
pygame
Fullscreen animated UI
OpenCV
Camera capture & image ops
FACE ATTENDANCE KIOSK
08 / 14

## Slide 9
ATTENDANCE
One clean sheet per day
Name
Category
Time
Anirudha Sarkar
Signass Student
07:30 AM
Aditya Talukdar
Students
07:42 AM
Sharanya Saha
Students
07:55 AM
Rohan Bose
Students
08:10 AM
Sukanya Das
Students
08:20 AM
Bipasa Paul
Students
08:27 AM
attendance/2026-07-17.csv
Marked once per day
A second sighting shows “already marked” — never a duplicate row.
Survives restarts
On launch it reloads today's file and picks up exactly where it left off.
Rolls over at midnight
A fresh sheet each day; the group folder is saved as the category.
FACE ATTENDANCE KIOSK
09 / 14

## Slide 10
PERFORMANCE
Engineered to stay smooth on a Pi
BEFORE
Recognition ran inline — froze the UI ~½ s each try
Camera reads blocked the main loop
Face mesh ran on the full 640×480 frame
Only one recognition attempt every 0.6 s
AFTER
Recognition on a background worker — UI never stalls
Dedicated capture thread always holds the latest frame
Mesh runs on a 320×240 frame (~4× lighter)
Four attempts a second, frame-rate capped at 30
2.4×
faster recognition cadence
3
concurrent threads: capture · match · UI
0
UI freezes during a scan
FACE ATTENDANCE KIOSK
10 / 14

## Slide 11
CONCURRENCY
Three threads, zero freezes
THREAD 1 — CAMERA GRABBER
Reads the camera continuously and keeps only the newest frame — the rest of the app never waits on camera I/O.
THREAD 2 — RECOGNITION WORKER
Every 0.25 s: detect → encode → match. All dlib calls sit behind a single lock — its C++ core is not thread-safe.
THREAD 3 — UI / MAIN LOOP
The pygame state machine draws the eyes and screens at a steady 30 FPS, whatever recognition is doing.
latest frame · lock-protected handoff
match result · polled, non-blocking
30 FPS
steady UI, always
4×/s
recognition attempts
0
freezes during a scan
FACE ATTENDANCE KIOSK
11 / 14

## Slide 12
FEATURES
More than a doorbell
Live enrollment
E
Capture a new student at the kiosk — saved and matched instantly.
Hot reload
R
Rescan the face database in the background, no restart.
Idle stats
Today's headcount and recent arrivals on the home screen.
Face tracking
Cyan eyes follow the visitor's face in real time.
Group filtering
Loads only chosen folders — Signass Student, Students.
Debug view
D
Live camera, face mesh and an FPS counter overlay.
FACE ATTENDANCE KIOSK
12 / 14

## Slide 13
TESTING
Proven with real students
TEST SCENARIOS
TC-01
Enrolled student recognized & marked
PASS
TC-02
Re-appearance → “already marked”, no duplicate
PASS
TC-03
Unknown face rejected after 5 s
PASS
TC-04
Kiosk enrollment (E) — matched on next attempt
PASS
TC-05
Folder reload (R) picks up new photos
PASS
TC-06
Phone photos with EXIF rotation
PASS
TC-07
Midnight rollover starts a fresh sheet
PASS
CASE STUDY
The sideways-photo bug
New photos taken on a phone loaded with zero faces detected. Phones store the image sideways and rely on an EXIF tag to rotate it — the loader ignored the tag, so the detector saw a rotated face and gave up.
The fix: apply the EXIF transpose before detection, and downscale 12 MP photos to 800 px first.
0 → 3
photos detected, of 3
71→9 s
database reload (8×)
FACE ATTENDANCE KIOSK
13 / 14

## Slide 14
UNDER THE HOOD
Modules & what's next
ARCHITECTURE
main.py
State machine & orchestration
bot_vision.py
Camera, tracking, recognition, enrollment
bot_eyes.py
pygame UI — eyes, greeting, overlays
bot_attendance.py
Daily CSV logging & de-duplication
config.py
Tunable settings & colour theme
ROADMAP
Export / sync attendance to Google Sheets
Multi-face handling for busy entrances
Liveness check to resist photo spoofing
Lightweight web dashboard for monitoring
On-device attendance — eyes and all.
FACE ATTENDANCE KIOSK
14 / 14